## Slide 1: KLH University Department of Electronics & Communication Engineering
PERSONALISED FEDERATED DEEP LEARNING FOR WIRELESS LINK QUALITY PREDICTION UNDER NON-IID CELL DATA
A Project Report submitted in partial fulfilment of the requirements for the course
MACHINE LEARNING
Course code: 25SC2107E | Academic year: 2026–27
SUBMITTED BY
N. PRANAY CHOWDARY — Roll No. 2520040009
P. SIDHU BHAGAVAN — Roll No. 2520040095
P. MOHAN — Roll No. 2520040045
UNDER THE GUIDANCE OF
Mr. N Lava Prasad
Assistant Professor

## Slide 2: Problem Statement and Objectives
Objectives
The problem
•
•
•
Wi-Fi signal strength changes from place to place and device to device.
Pooling raw data from every device raises privacy and communication concerns.
Federated learning keeps data on each client, but client data are non-IID, so one global model may fit some clients poorly.
Classify Wi-Fi link quality (Poor, Fair, Good, Excellent) from RSSI.
Compare Centralized MLP, FedAvg and FedPer on non-IID clients.
Build a hybrid: RSSI rule plus personalised models near boundaries.
Key question: does personalisation help when client data are non-IID?
Run locally with a health check and a prediction API.

## Slide 3: Literature Background
McMahan et al. (2017)
FedAvg · AISTATS
Clients train locally and the server averages their model weights, cutting communication cost.
Arivazhagan et al. (2019)
FedPer
Shares base layers across clients but keeps personalisation layers local to each client.
Li et al. (2020)
FedProx · MLSys
Addresses uneven clients and data. Background only; not one of our compared methods.
Non-IID Survey (2021)
Federated Learning on Non-IID Data: A Survey
Reviews how non-IID data hurts federated learning and the methods proposed to handle it.
Torres-Sospedra et al. (2014)
UJIIndoorLoc
Multi-building, multi-floor Wi-Fi fingerprint database. This is our data source.

## Slide 4: Key Terms in Plain Language
RSSI
Received Signal Strength Indicator, in dBm. Closer to 0 is stronger (−50 beats −80).
WAP
Wireless Access Point: a Wi-Fi router or device that a phone can hear.
Wi-Fi fingerprint
The RSSI values from many WAPs at one measurement. One row of the dataset.
Federated client
A data owner that trains locally. Here, one PHONEID group (simulated).
Non-IID
Clients' data differ, for example in class mix, so they are not like random draws from one pool.
Wi-Fi, not cellular
RSSI here is Wi-Fi. CQI, RSRP and RSRQ are cellular measures and are not used.
Sources: Torres-Sospedra et al. (2014); Federated Learning on Non-IID Data: A Survey (2021).

## Slide 5: Dataset Overview: UJIIndoorLoc
520
WAP columns (up to)
19,937
samples in the class analysis
16
PHONEID groups = simulated clients
2 files
trainingData.csv and validationData.csv
Why this dataset
•
•
•
•
Public Wi-Fi fingerprint dataset with RSSI from many WAPs.
The PHONEID column gives natural groups that can act as clients.
Measured RSSI readings, not simulated signals.
Wi-Fi only: no cellular CQI, RSRP or RSRQ.
Sources: Torres-Sospedra et al. (2014), UJIIndoorLoc.
5

## Slide 6: Exploratory Data Analysis Findings
Class distribution (19,937 samples)
Excellent (42.0%)
8,366
Class imbalance
Excellent is 42.0% of samples; Poor is only 6.4% (1,281).
Good (36.4%)
7,256
RSSI and access points
Not-detected WAPs are stored as 100 (−100 dBm). 55 of up to 520 WAP columns are constant, so 465 are kept.
Fair (15.2%)
3,034
Poor (6.4%)
1,281
Clients differ (non-IID)
The 16 PHONEID groups differ in sample size and in class mix.
Sources: UJIIndoorLoc (Torres-Sospedra et al., 2014); class counts from this project's analysis.

## Slide 7: Preprocessing and Feature Engineering
1
Load data
2
Fix missing RSSI
trainingData.csv and validationData.csv
Sentinel value 100 (not detected) becomes −100 dBm
3
Drop constant columns
55 columns never change, so they carry no signal
4
Add summary features
Seven summary values computed per fingerprint
5
Scale inputs
Saved MinMaxScaler scales every model input
520
WAP columns (up to)
−100
dBm replaces 100
465
columns kept
+7
summary features
472
total model inputs

## Slide 8: RSSI Thresholds for the Four Classes
Poor
below −75 dBm
Fair
−75 to below −65 dBm
Good
−65 to below −55 dBm
Excellent
−55 dBm or stronger
−75 dBm
−65 dBm
−55 dBm
weaker signal
stronger signal
Uses maximum RSSI
Each row is labelled by the strongest RSSI among its WAPs.
Edge values
Exactly −75 dBm is Fair, −65 is Good, and −55 is Excellent.
Wi-Fi, not cellular
These are Wi-Fi RSSI limits in dBm, not CQI, RSRP or RSRQ.

## Slide 9: Federated Learning Workflow
1 16 simulated clients (PHONEID groups)
2
Client 1
own data, local training
Client 2
own data, local training
Client 16
3
Server
averages model weights (FedAvg, McMahan et al., 2017)
own data, local training
5
Evaluation
accuracy, balanced accuracy and weighted F1 on test data
Simulation: clients are PHONEID groups, not live devices.
4 Updated model goes back to clients; repeat for several rounds

## Slide 10: Four Methods Compared
 | Centralized MLP | FedAvg | FedPer | Hybrid
Training data | Pooled in one place | Stays on each client | Stays on each client | Same as FedPer
Model | One MLP | One shared global model | Shared base + client layers | RSSI rule + client models
Personalised? | No | No | Yes | Yes, near thresholds
Main idea | Reference with all data together | Average everyone's weights | Share the base, keep a personal head | Rule for clear cases, model for close calls
Sources: McMahan et al. (2017); Arivazhagan et al. (2019).

## Slide 11: FedPer Explained Simply
Input
472 features
Client 1 layers
Shared base layers same for every client server averages them
Client 2 layers
Client 16 layers
Output Poor Fair Good
Excellent
Shared base
averaged by the server across clients
Personal layers
stay on the client, tuned to its data
Why it helps
client data differ (non-IID)
Sources: Arivazhagan et al. (2019), Federated Learning with Personalization Layers.
11

## Slide 12: Results Comparison
Reported metrics by method (%)
97.93
98.42
97.94
100
93.13
92.91 93.13
89.06
89.37
89.02
82.89 82.73 82.65
Percent (%)
80
60
40
20
0
Centralized MLP
FedAvg
FedPer
Hybrid
Accuracy (%) Balanced accuracy (%) Weighted F1 (%)
Hybrid was evaluated on 2,998 test rows. All metrics measure agreement with RSSI-threshold labels, not real internet speed.

## Slide 13: Hybrid Prediction Logic
New Wi-Fi fingerprint max RSSI and client (PHONEID)
Is max RSSI within 0.25 dBm of a threshold?
No
Clear case
use the RSSI rule label
±0.25 dBm
boundary margin around each threshold (−75, −65,
−55)
Yes (close to a threshold)
Yes
Use that client's personalised model
Known client with an available personalised model?
No
Fallback: use the RSSI rule
unknown client or no model

## Slide 14: How to Run and Check the Project
1
python run.py
Start the project from its folder
2
http://127.0.0.1:8000
Open the app in a web browser
3
/docs
API documentation page
4
/api/health
Check that the service is running
5
/api/predict
Request a link-quality prediction

## Slide 15: Conclusion, Limitations and Future Work
Conclusion
•
•
•
FedPer (89.06%) beats FedAvg (82.89%) on non-IID clients.
Centralized MLP: 93.13% reference.
Hybrid: 97.93% on 2,998 test rows.
Limitations
•
•
•
•
Labels come from RSSI rules, so accuracy is not real speed or user experience.
Clients are simulated PHONEID groups.
No live federated training.
Wi-Fi RSSI only, not CQI, RSRP or RSRQ.
Future work
•
•
•
•
Check labels against measured throughput.
Test on real cellular measures.
Compare more methods, such as FedProx.
Pilot on real devices.